OpenGL for absolute beginners.

---
What is OpenGL?

---
From the Red book:
OpenGL is a software interface to graphics hardware.

---
A state machine.

---
        glViewport (0, 0, w, h)
        glMatrixMode (GL_PROJECTION)
        glLoadIdentity ()
        glFrustum (-1.0, 1.0, -1.0, 1.0, 1.5, 20.0)
        glMatrixMode (GL_MODELVIEW)
        glScalef (1.0, 2.0, 1.0)

---
Client-server Architecture
Applications are clients.

---
High Level.

---
Low Level.

---
What it cannot do...

---
Can't open a window.

---
Can't handle user input.

---
Can't even draw sophisticated 3D models on it's own.

---
What can OpenGL do?

---
Think Lego (TM)

---
Wireframe model

---
Wireframe model with depth cues

---
Anti aliasing

---
Color (Flat)

---
Lighting and smooth shading

---
Textures and shadows

---
Motion blur

---
Zoom in

---
Effects

---
More at:
http://fly.cc.fer.hr/~unreal/theredbook/appendixj.html

---
Disclaimer
Python, GLUT, GLU

---
Disclaimer
OpenGL ES code using OpenGL

---
Hello OpenGL

---
   # clear all pixels
   glClear(GL_COLOR_BUFFER_BIT)
   # Specify the vertices (in this case just one) as an array, as in (x, y)
   vertices = [0,0]
   glVertexPointer(2, GL_SHORT, 0, vertices)
   # Enable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Set the drawing color
   glColor3f(1, 0, 0)
   # Draw the vertices
   glDrawArrays(GL_POINTS, 0, 1)
   # Disable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # don't wait!
   # start processing buffered OpenGL routines
   glFlush()

---
Four points

---
   # clear all pixels
   glClear(GL_COLOR_BUFFER_BIT)
   # Specify the vertices (in this case four) as an array, as in (x, y)
   vertices = [-0.8,0.8, 0.8,0.8, 0.8,-0.8, -0.8,-0.8]
   glVertexPointer(2, GL_FLOAT, 0, vertices)
   # Enable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Set the drawing color
   glColor3f(1, 0, 0)
   # Draw the vertices
   glDrawArrays(GL_POINTS, 0, len(vertices)/2)
   # Disable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # don't wait!
   # start processing buffered OpenGL routines
   glFlush();

---
A rectangle

---
   # clear all pixels
   glClear(GL_COLOR_BUFFER_BIT)
   # Specify the vertices (in this case four) as an array, as in (x, y)
   vertices = [-0.8,0.8, 0.8,0.8, 0.8,-0.8, -0.8,-0.8]
   glVertexPointer(2, GL_FLOAT, 0, vertices)
   # Enable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Set the drawing color
   glColor3f(1, 0, 0)
   # Draw the vertices
   glDrawArrays(GL_LINE_LOOP, 0, len(vertices)/2)
   # Disable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # don't wait!
   # start processing buffered OpenGL routines
   glFlush();

---
Animation

---
def display(i):
   # clear all pixels
   glClear(GL_COLOR_BUFFER_BIT)
   # Prevent the box from going out of the screen
   clipToWindow()
   glMatrixMode(GL_MODELVIEW)
   glLoadIdentity()
   glTranslate(xPosition, yPosition, 0);
   # Specify the vertices (in this case just one) as an array, as in (x, y)
   vertices = [0, 0,
        0, 50,
        50, 50,
        50, 0]
   glVertexPointer(2, GL_FLOAT, 0, vertices)
   # Enable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Set the drawing color
   glColor3f(1, 0, 0)
   # Draw the vertices
   glDrawArrays(GL_TRIANGLE_FAN, 0, len(vertices)/2)
   # Disable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Swap the buffers (glFLush() implicit)
   glutSwapBuffers();
   # Compute the new position
   updatePosition()
   glutTimerFunc(t, display, 1)

---
def reshape(width, height):
  # Setup the drawing area (bottomX bottomY, topX, topY)
  glViewport(0, 0, width, height)
  # Update the screen width and height
  global screenWidth, screenHeight
  screenWidth = width
  screenHeight = height
  # Define the clipping volume (left, right, bottom, top, near, far)
  glMatrixMode(GL_PROJECTION)
  glLoadIdentity()
  glOrtho(0, width, 0, height, -1, 1);
  # Initialize the model-view matrix
  glMatrixMode(GL_MODELVIEW)
  glLoadIdentity();

---
Setting up the canvas.

---
The Camera Analogy
(Illustration from the red book)

---
The duality of modeling and viewing.
(Illustration from the red book)

---
Perspective projection
(illustration from the red book)

---
Orthographic Projection
(illustration from the red book)

---
Viewport transformation
(illustration from the red book)