OpenGL for absolute beginners.

---
What is OpenGL?

---
From the Red book:
OpenGL is a software interface to graphics hardware.
[Speaker Notes: OpenGL is not a language. It's just a specification of an API that vendors implement on their platforms. So it is platform and language independent. In your operating system the component that implements OpenGL is the graphics driver.]

---
(Diagrams from the super bible)
[Speaker Notes: There are OpenGL implementations independent of any hardware. The OpenGL commands in such an implementation are handled by a software rasterizer which then sends the final image to the native graphics API. On platforms that have OpenGL enabled hardware, OpenGL commands are directly sent to the display device.]

---
A state machine.

---
        glViewport (0, 0, w, h)
        glMatrixMode (GL_PROJECTION)
        glLoadIdentity ()
        glFrustum (-1.0, 1.0, -1.0, 1.0, 1.5, 20.0)
        glMatrixMode (GL_MODELVIEW)
        glScalef (1.0, 2.0, 1.0)
[Speaker Notes: Most OpenGL commands are dependent on the current state of the OpenGL context. Note how we first change the current matrix mode and then apply transformations to it.]

---
A pipeline.
(Illustration from the super bible)
[Speaker Notes: Note that all OpenGL commands are first buffered before they are processed. Also note that this is very simplified version of the pipeline. We will see a detailed diagram later.]

---
Client-server Architecture
Applications are clients.
[Speaker Notes: An OpenGL program is in theory a client. The results of the commands invoked by the client will be seen on a server. In most cases the client and the server are the same machine. But it is possible to separate them.]

---
High Level.
[Speaker Notes: When drawing in OpenGL we don't think in terms of pixels at all. We specify our scene using primitives like points and lines in a coordinate system. OpenGL takes care of mapping them to actual pixel values.]

---
Low Level.
[Speaker Notes: Though we don't have to worry about pixels, we still cannot draw objects directly. For instance, there aren't any OpenGL commands for even mundane things like drawing a cube or drawing a circle. Any object has to be specified using a set of primitives.]

---
What it cannot do...

---
Can't open a window.
[Speaker Notes: Since OpenGL has to be platform independent, it leaves all the platform specific functions like windowing, I/O, audio etc. to the host operating system.]

---
Can't handle user input.

---
Can't even draw sophisticated 3D models on it's own.
[Speaker Notes: Most of the detailed graphics that we see in games like Doom 3D are actually generated using other software like 3D studio Max, serialized and then loaded at runtime.]

---
What can OpenGL do?

---
Think Lego (TM)
[Speaker Notes: Children build amazing structures using simple, unimpressive by themselves, and identical blocks. Another analogy is the bricks that are used to build sky scrapers and even the pyramids. The same principle applies to drawing objects with OpenGL.]

---
Wireframe model
[Speaker Notes: Plate 1 shows an entire scene displayed as a wireframe model—that is, as if all the objects in the scene were made of wire. Each line of wire corresponds to an edge of a primitive (typically a polygon). For example, the surface of the table is constructed from triangular polygons that are positioned like slices of pie. Note that you can see portions of objects that would be obscured if the objects were solid rather than wireframe. For example, you can see the entire model of the hills outside the window even though most of this model is normally hidden by the wall of the room. The globe appears to be nearly solid because it’s composed of hundreds of colored blocks, and you see the wireframe lines for all the edges of all the blocks, even those forming the back side of the globe. The way the globe is constructed gives you an idea of how complex objects can be created by assembling lower-level objects.]

---
Wireframe model with depth cues
[Speaker Notes: Plate 2 shows a depth-cued version of the same wireframe scene. Note that the lines farther from the eye are dimmer, just as they would be in real life, thereby giving a visual cue of depth. OpenGL uses atmospheric effects (collectively referred to as fog) to achieve depth cueing.]

---
Anti aliasing
[Speaker Notes: Plate 3 shows an antialiased version of the wireframe scene. Antialiasing is a technique for reducing the jagged edges (also known as jaggies) created when approximating smooth edges using pixels—short for picture elements—which are confined to a rectangular grid. Such jaggies are usually the most visible, with near-horizontal or near-vertical lines.]

---
Color (Flat)
[Speaker Notes: Plate 4 shows a flat-shaded, unlit version of the scene. The objects in the scene are now shown as solid. They appear “flat” in the sense that only one color is used to render each polygon, so they don’t appear smoothly rounded. There are no effects from any light sources.]

---
Lighting and smooth shading
[Speaker Notes: Plate 5 shows a lit, smooth-shaded version of the scene. Note how the scene looks much more realistic and three-dimensional when the objects are shaded to respond to the light sources in the room, as if the objects were smoothly rounded.]

---
Textures and shadows
[Speaker Notes: Plate 6 adds shadows and textures to the previous version of the scene. Shadows aren’t an explicitly defined feature of OpenGL (there is no “shadow command”), but you can create them yourself using the techniques described in Chapter 9 and Chapter 14 of the red book. Texture mapping allows you to apply a two-dimensional image onto a three-dimensional object. In this scene, the top on the table surface is the most vibrant example of texture mapping. The wood grain on the floor and table surface are all texture mapped, as well as the wallpaper and the toy top (on the table).]

---
Motion blur
[Speaker Notes: Plate 7 shows a motion-blurred object in the scene. The sphinx appears to be captured moving forward, leaving a blurred trace of its path of motion.]

---
Zoom in
[Speaker Notes: Plate 8 shows the scene as it was drawn for the cover of the book from a different viewpoint. This plate illustrates that the image really is a snapshot of models of three-dimensional objects.]

---
Effects
[Speaker Notes: Plate 9 brings back the use of fog, which was shown in Plate 2 to simulate the presence of smoke particles in the air. Note how the same effect in Plate 2 now has a more dramatic impact in Plate 9.]

---
More at:
http://fly.cc.fer.hr/~unreal/theredbook/appendixj.html
[Speaker Notes: All the above images and illustrations were taken directly from the red book.]

---
Disclaimer
Python, GLUT
[Speaker Notes: We use Python because that is the common factor among our team. Also, it is relatively easier to setup OpenGL with Python. For managing windows and I/O, we use GLUT as provided in the PyOpenGL module. Note that there are other libraries like GLU, SDL, EGL, AGL, WGL and GLX that are widely used with OpenGL too, but we will avoid them.]

---
Disclaimer
OpenGL ES code using OpenGL
[Speaker Notes: Since our target platforms are mostly mobile, desktop OpenGL is mostly irrelevant. Also, most desktop code uses OpenGL ES style code as a best practice anyway. But on a practical note we made this choice because each mobile platform has it's own method of setup and since our main aim is to learn the concepts we wanted to avoid too many specifics.]

---
Hello OpenGL
[Speaker Notes: Here we'll look at a minimal OpenGL program. All it does is draw a point on the screen.]

---
   # clear all pixels
   glClear(GL_COLOR_BUFFER_BIT)
   # Specify the vertices (in this case just one) as an array, as in (x, y)
   vertices = [0,0]
   glVertexPointer(2, GL_SHORT, 0, vertices)
   # Enable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Set the drawing color
   glColor3f(1, 0, 0)
   # Draw the vertices
   glDrawArrays(GL_POINTS, 0, 1)
   # Disable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # don't wait!
   # start processing buffered OpenGL routines
   glFlush()

---
[Speaker Notes: All OpenGL function names conform to this convention. The last two parts of the function, number of arguments and type of arguments, are optional. Functions are usually known by their root name since multiple variations may exist.]

---
Four points

---
   # clear all pixels
   glClear(GL_COLOR_BUFFER_BIT)
   # Specify the vertices (in this case four) as an array, as in (x, y)
   vertices = [-0.8,0.8, 0.8,0.8, 0.8,-0.8, -0.8,-0.8]
   glVertexPointer(2, GL_FLOAT, 0, vertices)
   # Enable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Set the drawing color
   glColor3f(1, 0, 0)
   # Draw the vertices
   glDrawArrays(GL_POINTS, 0, len(vertices)/2)
   # Disable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # don't wait!
   # start processing buffered OpenGL routines
   glFlush();
[Speaker Notes: Drawing in OpenGL is a two step process: Specify a list of points. Join them. It's akin to the many 'connect the dots' puzzles found in children's magazines. Specifying four points first step in drawing a rectangle.]

---
A rectangle

---
   # clear all pixels
   glClear(GL_COLOR_BUFFER_BIT)
   # Specify the vertices (in this case four) as an array, as in (x, y)
   vertices = [-0.8,0.8, 0.8,0.8, 0.8,-0.8, -0.8,-0.8]
   glVertexPointer(2, GL_FLOAT, 0, vertices)
   # Enable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Set the drawing color
   glColor3f(1, 0, 0)
   # Draw the vertices
   glDrawArrays(GL_LINE_LOOP, 0, len(vertices)/2)
   # Disable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # don't wait!
   # start processing buffered OpenGL routines
   glFlush();
[Speaker Notes: Connect the four points in a loop to draw a rectangle.]

---
Drawing primitives
[Speaker Notes: As said before, OpenGL can only draw a few predefined primitives. The ones supported by OpenGL ES are points, lines, line strip, line loop, triangles, triangle strip and triangle fan. No matter how complex your final objects needs to be, it will have to be constructed from these primitives.]

---
# Declare initial window size, position, and display mode
# (single buffer and RGBA). Open window with "hello"
# in its title bar. Call initialization routines.
# Register callback function to display graphics.
# Enter main loop and process events.
glutInit(sys.argv)
glutInitDisplayMode(GLUT_SINGLE | GLUT_RGB)
glutInitWindowSize(250, 250)
glutInitWindowPosition(100, 100)
glutCreateWindow("hello")
glutDisplayFunc(display)
glutMainLoop()
[Speaker Notes: Pay attention to these lines (you'll find them in the end of the file) They are not OpenGL functions, they belong to the GLUT API.]

---
GLUT (OpenGL Utility Toolkit):

---
Animation

---
def display(i):
   # clear all pixels
   glClear(GL_COLOR_BUFFER_BIT)
   # Prevent the box from going out of the screen
   clipToWindow()
   glMatrixMode(GL_MODELVIEW)
   glLoadIdentity()
   glTranslate(xPosition, yPosition, 0);
   # Specify the vertices (in this case just one) as an array, as in (x, y)
   vertices = [0, 0,
        0, 50,
        50, 50,
        50, 0]
   glVertexPointer(2, GL_FLOAT, 0, vertices)
   # Enable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Set the drawing color
   glColor3f(1, 0, 0)
   # Draw the vertices
   glDrawArrays(GL_TRIANGLE_FAN, 0, len(vertices)/2)
   # Disable vertex arrays
   glEnableClientState(GL_VERTEX_ARRAY)
   # Swap the buffers (glFLush() implicit)
   glutSwapBuffers();
   # Compute the new position
   updatePosition()
   glutTimerFunc(t, display, 1)

---
def reshape(width, height):
  # Setup the drawing area (bottomX bottomY, topX, topY)
  glViewport(0, 0, width, height)
  # Update the screen width and height
  global screenWidth, screenHeight
  screenWidth = width
  screenHeight = height
  # Define the clipping volume (left, right, bottom, top, near, far)
  glMatrixMode(GL_PROJECTION)
  glLoadIdentity()
  glOrtho(0, width, 0, height, -1, 1);
  # Initialize the model-view matrix
  glMatrixMode(GL_MODELVIEW)
  glLoadIdentity();

---
Setting up the canvas.

---
The Camera Analogy
(Illustration from the red book)

---
The duality of model and view.
(Illustration from the red book)

---
Perspective projection
(illustration from the red book)

---
Orthographic Projection
(illustration from the red book)

---
Viewport transformation
(illustration from the red book)